## Slide 1: Introduction to Processor Architecture (EC2.204)
Lecture 2 – instruction set architecture
Deepak Gangadharan
Computer Systems Group (CSG), IIIT Hyderabad
Slide Contents: Based on materials from text books and other public sources

## Slide 2: ISA: Hardware – Software Interface

## Slide 3: Programming Languages and Abstractions
A Programming Language provides
Data Abstractions
  int, float, bool etc. data types.
  Mechanism for hierarchical composition of new Data Abstractions
    Structures, arrays, Unions etc.
Data Processing Abstractions
  Arithmetic and Boolean Operations, String Operations etc.
Control Abstractions – while, if, for constructs etc.
Key Idea: We should be able
to realize these abstractions
through the ISA of a given processor!

## Slide 4: ISA Design Philosophy
Two ISA design philosophies
  RISC – Reduced Instruction Set Computer
  CISC – Complex Instruction Set Computer

## Slide 5: RISC versus CISC
RISC | CISC
Each instruction does one simple task. | Each instruction can do multiple tasks.
Amount of work done in each instruction is roughly the same. | Amount of work done in each instruction could have huge variance.
Fixed Length instruction format. | Variable length instruction format.
Load-Store Architecture. Instruction operands should always reside in registers. | Instruction Operands can reside in memory also.
Large bank of general purpose registers. | Many special purpose registers.
Simple Addressing Modes. | Can have complex addressing modes.
Few Data Types (typically integer and float) | Could provide support for more data types like Strings.
Berkeley RISC , Stanford MIPS, ARM, HP’s PA-RISC | Intel x86 line of processors

## Slide 6: RISC or CISC – Which way should we go?
RISC | CISC
Simple, fast (pipelined) and power efficient hardware implementations. | Complex hardware, not so power efficient, hard to come up with pipelined implementations.
Not so good for an Assemble Language Programmer when compared with CISC ISAs. | Good for an Assemble Language Programmer.
Good for compiler writer. | Compiler writer has to work hard to use the underlying CISC ISA features.
Less code density | Good code density

## Slide 7: Assembly Language Example

## Slide 8: Assembly/Machine Code View
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic or logical operation
    Used for conditional branching
CPU
PC
Registers
Memory
Code
Data
Stack
Addresses
Data
Instructions
Condition
Codes
  Memory
    Byte addressable array
    Code and user data
    Stack to support procedures

## Slide 9: 8-bit, 16-bit, 32-bit, 64-bit ISAs
A processor supporting a 32-bit ISA
Registers are 32 bits in length
32-bit ALU
Data bus width between processor and main memory 32 bits
Address space size 2^32 bytes [4 GB]
A 64-bit processor may support a 32-bit ISA also for compatibility reasons [but don’t expect performance gains]

## Slide 10: Intel x86 Processors
Dominate laptop/desktop/server market
Evolutionary design
  Backwards compatible up until 8086, introduced in 1978
  Added more features as time goes on
Complex instruction set computer (CISC)
  Many different instructions with many different formats
  Hard to match performance of Reduced Instruction Set Computers (RISC)
  But, Intel has done just that!
    In terms of speed. Less so for low power.

## Slide 11: Intel x86 Evolution: Milestones
Name Date Transistors MHz
8086 1978 29K 5-10
  First 16-bit Intel processor. Basis for IBM PC & DOS
  1MB address space
386 1985 275K 16-33
  First 32 bit Intel processor , referred to as IA32
  Added “flat addressing”, capable of running Unix
Pentium 4E 2004 125M 2800-3800
  First 64-bit Intel x86 processor, referred to as x86-64
Core 2 2006 291M 1060-3500
  First multi-core Intel processor
Core i7 2008 731M 1700-3900
  Four cores

## Slide 12: Intel x86 Processors, cont.
Machine Evolution
  386 1985 0.3M
  Pentium 1993 3.1M
  Pentium/MMX 1997 4.5M
  PentiumPro 1995 6.5M
  Pentium III 1999 8.2M
  Pentium 4 2001 42M
  Core 2 Duo 2006 291M
  Core i7 2008 731M
Added Features
  Instructions to support multimedia operations
  Instructions to enable more efficient conditional operations
  Transition from 32 bits to 64 bits
  More cores

## Slide 13: Assembly/Machine Code View
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic or logical operation
    Used for conditional branching
CPU
PC
Registers
Memory
Code
Data
Stack
Addresses
Data
Instructions
Condition
Codes
  Memory
    Byte addressable array
    Code and user data
    Stack to support procedures

## Slide 14: Accessing Information: IA32 Integer Registers
Used to store integer/pointers
  First six registers can be considered general purpose registers, except some instructions that uses specific registers as source and/or destination.
  Last two registers, contain pointers to important places in the program stack
  The low-order 2 bytes of the first four registers can be independently read or written by the byte operation instructions.
  Similarly, the low-order 16 bits of each register can be read or written by word operation instructions.

## Slide 15: Accessing Information: x86-64 Integer Registers
16 registers to store integer/pointers
  First six registers can be considered general purpose registers, except some instructions that uses specific registers as source and/or destination.
  Next two registers, contain pointers to important places in the program stack
  The low-order 2 bytes of the first four registers can be independently read or written by the byte operation instructions.
  Similarly, the low-order 16 bits of each register can be read or written by word operation instructions.

## Slide 16: General Purpose Registers
Accumulator register (ax). Used in arithmetic operations
Counter register (cx). Used in shift/rotate instructions and loops.
Data register (dx). Used in arithmetic operations and I/O operations.
Base register (bx). Used as a pointer to data
Stack Pointer register (sp). Pointer to the top of the stack.
Stack Base Pointer register (bp). Used to point to the base of the stack.
Source Index register (si). Used as a pointer to a source in stream operations.
Destination Index register (di). Used as a pointer to a destination in stream operations.
Source: Wikipedia

## Slide 17: Data Transfer Instructions

## Slide 18: movq Operand Combinations
Cannot do memory-memory transfer with a single instruction
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movq $0x4,%rax
temp = 0x4;
movq $-147,(%rax)
*p = -147;
movq %rax,%rdx
temp2 = temp1;
movq %rax,(%rdx)
*p = temp;
movq (%rax),%rdx
temp = *p;
Src,Dest

## Slide 19: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx

## Slide 20: Example of Simple Addressing Modes
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 21: Understanding Swap()
%rdi
%rsi
%rax
%rdx
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Memory
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Registers

## Slide 22: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 23: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 24: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 25: Understanding Swap()
456
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 26: Understanding Swap()
456
123
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 27: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Aha! Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx

## Slide 28: Complete Memory Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 16 integer registers
  Ri: Index register: Any, except for %rsp
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]

## Slide 29: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Carnegie Mellon
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x0100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 30: Data Transfer Instructions

## Slide 31: Example
Dereferencing a pointer  Copying the pointer into a register and using the register in a memory reference
Local variables are often stored in registers rather than memory locations  Faster access

## Slide 32: Push and Pop

## Slide 33: Push and Pop
subl $4,%esp
movl %eax,(%esp)

## Slide 34: Arithmetic and Logic Operations

## Slide 35: Address Computation Instruction
Carnegie Mellon
leaq Src, Dst
  Src is address mode expression
  Set Dst to address denoted by expression
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*y
      k = 1, 2, 4, or 8
  Compilers can use it for compact arithmetic operations
Example
long m12(long x)
{
return x*12;
}
leaq (%rdi,%rdi,2), %rax # t <- x+x*2
salq $2, %rax # return t<<2
Converted to ASM by compiler:

## Slide 36: Unary Operations
The single operand can either be a register or a memory location
Example: incl (%esp)  Increments the 4 byte element on top of the stack

## Slide 37: Some Arithmetic Operations
Carnegie Mellon
Two Operand Instructions:
  Format Computation
    addq Src,Dest Dest = Dest + Src
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
    salq Src,Dest Dest = Dest << Src Also called shlq
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    shrq Src,Dest Dest = Dest >> Src Logical
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
Watch out for argument order!
No distinction between signed and unsigned int (why?)

## Slide 38: Shift Operations

## Slide 39: Arithmetic Expression Example
Carnegie Mellon
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication
    But, only used once
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret

## Slide 40: Understanding Arithmetic Expression Example
Carnegie Mellon
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | t1, t2, rval
%rdx | t4
%rcx | t5
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}

## Slide 41: Condition Codes
CPU maintains a set of single-bit condition code registers describing attributes of the most recent arithmetic or logical operation.
These registers (listed below) can then be tested to perform conditional branches.

## Slide 42: Condition Codes
t = a + b

## Slide 43: Condition Codes
All unary and binary arithmetic & logical operations (except leaq) set the single bit condition codes.
For logical operations, the carry and overflow flags are set to zero.
Fore shift operations, the carry flag is set to the last bit shifted out, while the overflow flag is set to zero.
INC and DEC instruction set the overflow and zero flags but leave the carry flag unchanged.

## Slide 44: Condition Codes
Two instruction classes (CMP and TEST) set the condition codes.
CMP behave similar to SUB without altering the destination register.
TEST behave similar to AND without altering the destination register.

## Slide 45: Condition Codes
Three common ways to use the condition codes
  Set a single byte to 0 or 1 depending on some combination of condition codes (SET instructions)
  Conditionally jump to some other part of the program (Jump instructions)
  Conditionally move data (CMOVE instructions)

## Slide 46: Accessing the Condition Codes
Instruction suffixes refer to combination of condition codes and not the operand types.
Operand D refers to a single byte register or single byte memory location.

## Slide 47: Condition Codes

## Slide 48: JUMP Instruction
A JUMP instruction can cause the execution to switch to a completely new position in the program
Generally a label used in assembly code to indicate the jump destination
Addresses of jump targets determined during object code generation

## Slide 49: JUMP Instructions and Condition Codes

## Slide 50: JUMP Instruction Encoding
Two common encodings used are
  PC relative: Encodes the difference between the address of target instruction and address of instruction immediately following the jump
  Absolute address
Why relative to address of instruction immediately following jump?
Assembly code
Disassembled code
+

## Slide 51: JUMP Instruction Encoding
Disassembled version after linking
Advantages:
Instructions can be compactly encoded (requiring just 2 bytes)
Object code can be shifted to different positions in memory without alteration

## Slide 52: Implementing Conditional Branches with Conditional Control

## Slide 53: Implementing Conditional Branches with Conditional Control

## Slide 54: Implementing Conditional Branches with Conditional Control

## Slide 55: Conditional Branches with Conditional Move

## Slide 56: Conditional Branches with Conditional Move

## Slide 57: Conditional Branches with Conditional Move

## Slide 58: Conditional Branches: Do-While Loop

## Slide 59: Conditional Branches: While Loop

## Slide 60: Conditional Branches: Switch Statement

## Slide 61: Y86-64 Processor State
ZF
SF
OF
  Program Registers
    15 registers (omit %r15). Each 64 bits
  Condition Codes
    Single-bit flags set by arithmetic or logical instructions
      ZF: Zero SF:Negative OF: Overflow
  Program Counter
    Indicates address of next instruction
  Program Status
    Indicates either normal operation or some error condition
  Memory
    Byte-addressable storage array
    Words stored in little-endian byte order
RF: Program registers
CC: Condition codes
PC
DMEM: Memory
Stat: Program status
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%rax
%rcx
%rdx
%rbx
%rsp
%rbp
%rsi
%rdi

## Slide 62: Y86-64 Instructions
  Subset of x86-64 instruction set
    includes only 8-byte integer operations
    fewer addressing modes (second index register and scaling not supported)
    No transfer of immediate data to memory
    smaller set of operations

## Slide 63: Y86-64 Instruction Set #1
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
The register order in encoding here is correct - Verified
The register order in encoding here is correct - Verified

## Slide 64: Y86-64 Instructions
Format
  1–10 bytes of information read from memory
    Can determine instruction length from first byte
    Not as many instruction types, and simpler encoding than with x86-64
  Each accesses and modifies some part(s) of the program state

## Slide 65: Y86-64 Instruction Set #2
0
1
2
3
4
5
6
7
8
9
V
D
D
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
rmmovq rA, D(rB)
4
0
rA
rB
mrmovq D(rB), rA
5
0
rA
rB
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
rrmovq
2
0
cmovle
2
1
cmovl
2
2
cmove
2
3
cmovne
2
4
cmovge
2
5
cmovg
2
6

## Slide 66: Y86-64 Instruction Set #3
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
addq
6
0
subq
6
1
andq
6
2
xorq
6
3

## Slide 67: Y86-64 Instruction Set #4
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6

## Slide 68: Encoding Registers
Each register has 4-bit ID
  Same encoding as in x86-64
Register ID 15 (0xF) indicates “no register”
  Will use this in our hardware design in multiple places
%rax
%rcx
%rdx
%rbx
0
1
2
3
%rsp
%rbp
%rsi
%rdi
4
5
6
7
%r8
%r9
%r10
%r11
8
9
A
B
%r12
%r13
%r14
No Register
C
D
E
F

## Slide 69: Instruction Example
Addition Instruction
  Add value in register rA to that in register rB
    Store result in register rB
    Note that Y86-64 only allows addition to be applied to register data
  Set condition codes based on result
  e.g., addq %rax,%rsi Encoding: 60 06
  Two-byte encoding
    First indicates instruction type
    Second gives source and destination registers
addq rA, rB
6
0
rA
rB
Encoded Representation
Generic Form

## Slide 70: Arithmetic and Logical Operations
  Refer to generically as “OPq”
  Encodings differ only by “function code”
    Low-order 4 bytes in first instruction word
  Set condition codes as side effect
addq rA, rB
6
0
rA
rB
subq rA, rB
6
1
rA
rB
andq rA, rB
6
2
rA
rB
xorq rA, rB
6
3
rA
rB
Add
Subtract (rA from rB)
And
Exclusive-Or
Instruction Code
Function Code

## Slide 71: Move Operations
  Like the x86-64 movq instruction
  Simpler format for memory addresses
  Give different names to keep them distinct
rrmovq rA, rB
2
0
Register  Register
Immediate  Register
irmovq V, rB
F
rB
3
0
V
Register  Memory
rmmovq rA, D(rB)
4
0
rA
rB
D
Memory  Register
mrmovq D(rB), rA
5
0
rA
rB
D

## Slide 72: Move Instruction Examples
irmovq $0xabcd, %rdx
movq $0xabcd, %rdx
30 82 cd ab 00 00 00 00 00 00
X86-64
Y86-64
Encoding:
rrmovq %rsp, %rbx
movq %rsp, %rbx
20 43
mrmovq -12(%rbp),%rcx
movq -12(%rbp),%rcx
50 15 f4 ff ff ff ff ff ff ff
rmmovq %rsi,0x41c(%rsp)
movq %rsi,0x41c(%rsp)
40 64 1c 04 00 00 00 00 00 00
Encoding:
Encoding:
Encoding:

## Slide 73: Conditional Move Instructions
  Refer to generically as “cmovXX”
  Encodings differ only by “function code”
  Based on values of condition codes
  Variants of rrmovq instruction
    (Conditionally) copy value from source to destination register
rrmovq rA, rB
Move Unconditionally
cmovle rA, rB
Move When Less or Equal
cmovl rA, rB
Move When Less
cmove rA, rB
Move When Equal
cmovne rA, rB
Move When Not Equal
cmovge rA, rB
Move When Greater or Equal
cmovg rA, rB
Move When Greater
2
0
rA
rB
2
1
rA
rB
2
2
rA
rB
2
3
rA
rB
2
4
rA
rB
2
5
rA
rB
2
6
rA
rB

## Slide 74: Jump Instructions
  Refer to generically as “jXX”
  Encodings differ only by “function code” fn
  Based on values of condition codes
  Same as x86-64 counterparts
  Encode full destination address
    Unlike PC-relative addressing seen in x86-64
Jump (Conditionally)
jXX Dest
7
fn
Dest

## Slide 75: Jump Instructions
jmp Dest
7
0
Jump Unconditionally
Dest
jle Dest
7
1
Jump When Less or Equal
Dest
jl Dest
7
2
Jump When Less
Dest
je Dest
7
3
Jump When Equal
Dest
jne Dest
7
4
Jump When Not Equal
Dest
jge Dest
7
5
Jump When Greater or Equal
Dest
jg Dest
7
6
Jump When Greater
Dest

## Slide 76: Y86-64 Program Stack
  Region of memory holding program data
  Used in Y86-64 (and x86-64) for supporting procedure calls
  Stack top indicated by %rsp
    Address of top stack element
  Stack grows toward lower addresses
    Top element is at highest address in the stack
    When pushing, must first decrement stack pointer
    After popping, increment stack pointer
%rsp
•
•
•
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 77: Stack Operations
  Decrement %rsp by 8
  Store word from rA to memory at %rsp
  Like x86-64
  Read word from memory at %rsp
  Save in rA
  Increment %rsp by 8
  Like x86-64
pushq rA
A
0
rA
F
popq rA
B
0
rA
F

## Slide 78: Subroutine Call and Return
  Push address of next instruction onto stack
  Start executing instructions at Dest
  Like x86-64
  Pop value from stack
  Use as address for next instruction
  Like x86-64
call Dest
8
0
Dest
ret
9
0

## Slide 79: Miscellaneous Instructions
  Don’t do anything
  Stop executing instructions
  x86-64 has comparable instruction, but can’t execute it in user mode
  We will use it to stop the simulator
  Encoding ensures that program hitting memory initialized to zero will halt
nop
1
0
halt
0
0

## Slide 80: Status Conditions
Mnemonic | Code
ADR | 3
Mnemonic | Code
INS | 4
Mnemonic | Code
HLT | 2
Mnemonic | Code
AOK | 1
  Normal operation
  Halt instruction encountered
  Bad address (either instruction or data) encountered
  Invalid instruction encountered
Desired Behavior
  If AOK, keep going
  Otherwise, stop program execution

## Slide 81: Y86-64 program

## Slide 82: Summary
Y86-64 Instruction Set Architecture
  Similar state and instructions as x86-64
  Simpler encodings
  Somewhere between CISC and RISC
How Important is ISA Design?
  Less now than before
    With enough hardware, can make almost anything go fast

## Slide 83
Thank You!